## Slide 1: MPEG Extensions to glTF2.0
Presentation to Khronos 3D Formats Group
12th May 2026

## Slide 2: Agenda
Introduction to MPEG and Work
MPEG-I Scene Description – Existing Extensions
Latest Extensions submitted to Khronos
Resources

## Slide 3
WG 2 MPEG
Technical
Requirements
SC29
MPEG organization under ISO/IEC JTC1/ SC29
Igor Curcio, WG2 Convenor
Youngkwon Lim, WG3 Convenor
Lu Yu, WG4 Convenor
Jens-Rainer Ohm, WG5 Convenor
Thomas Sporer, WG6 Convenor
Marius Preda, WG7 Convenor
Marco Mattavelli, WG8 Convenor
Jörn Ostermann, AG2 Convenor
Kyuheon Kim, AG3 Convenor
AG 5 MPEG
Visual Quality
Assessment
Mathias Wien, AG5 Convenor
WG 3 MPEG
Systems
WG 4 MPEG
Video Coding
WG 5 Joint Video
Coding Team
with ITU
Gary Sullivan, SC29 Chairman
WG 6 MPEG
Audio Coding
WG 7 MPEG
Coding for 3D
Graphics and
Haptics
WG 8 MPEG
Genomic Coding
AG 3 MPEG
Liaison and
Communication
AG 2 MPEG
Technical
Coordination

## Slide 4
2025
2026
2027
2028
2029
149
153
157
161
150
151
152
154
155
156
158
159
160
MPEG meeting:
MPEG Immersive Video v.2
Media Coding
Scene Description with Advanced Interactivity
Media authenticity and provenance indication
Enhanced Geometry-based PCC (advanced compression tools)
Omnidirectional MediA Format (OMAF) – Server-Side Dynamic Adaptation
Video Decoding Interface
Beyond Media
Systems and Tools
6 DoF Audio v.2
Video Coding for Machines
Carriage of Dynamic Mesh Compression
Green metadata v.4
Immersive Haptics
Carriage of Haptics Data
Compression of LIDAR
164
162
163
Open Font Format v.5
DASH v.7
File Format (ISOBMFF) v.10
Graph genome support
New search capabilities of genomic data
AI Graphics Compression
Feature Coding for Machines
Video coding optimizations for machine analysis
Lenslet video coding
Biomedical waveform coding (BWC)
Avatar representation formats
165
Dynamic Mesh Compression
Solid Point Cloud Coding
Video-based Gaussian Splat Coding
Geometry based Gaussian Splat Coding
Audio Authenticity
CMAF v.4

## Slide 5
2025
2026
2027
2028
149
153
157
161
150
151
152
154
155
156
158
159
160
MPEG meeting:
Neural network-based video compression
Major Maintenance and Extensions
Explorations
Enhanced compression beyond VVC capabilities
Video supplemental enhancement information v5
AI support for representation and search of genomic data
Management of privacy and protection of genomic data
Systems Technologies for AI-based Compression
Versatile Video Coding v 4
Compression of neural networks
Coding for Gaussian Splat
Audio Coding for Machines
High Efficiency Video Coding Extensions
Advanced Video Coding Extensions
6G opportunities
Media type independent metadata
AI reproducibility
Application Metadata Carriage
Animation compression

## Slide 6: First edition extension
scene
node
mesh
accessor
bufferView
buffer
MPEG_buffer_circular
MPEG_mesh_linking
MPEG_accessor_timed
MPEG_media
MPEG_audio_spatial
MPEG_scene_dynamic
light
camera
material
technique
program
shader
texture
MPEG_texture_video
animation
skin
source
image
MPEG_viewport _recommended
MPEG_audio_spatial
MPEG_animation_timing
Core Extensions
https://www.khronos.org/events/gltf-meetup-July2023

## Slide 7: Second Edition - Formalitities
ISO/IEC DIS 23090-14:2025 Information technology — Coded representation of immersive media — Part 14: Scene description
  Editors: Bouazizi Imed Dr, Hirtzlin Patrice M., Stockhammer Thomas Mr Dr.
  https://sd.iso.org/projects/project/90191/overview
  Published 2025-11-06
ISO/IEC DIS 23090-14/AWI Amd 1: Information technology — Coded representation of immersive media — Part 14: Scene description — Amendment 1: Support of MPEG-I audio, scene understanding and other extensions
  Editors: Bouazizi Imed Dr, Lelievre Sylvain M.
  https://sd.iso.org/projects/project/90213/overview
  Sent for final ballot 2026-05-07
ISO/IEC 23090-24 Information technology — Coded representation of immersive media — Part 24: Conformance and reference software for scene description — Amendment 1: Conformance and reference software for scene description on haptics, augmented reality, avatars, interactivity and lighting
  Editors: Imed Bouazizi, Gurdeep Singh Bhullar
  https://sd.iso.org/projects/project/87584/overview
  Expect publication 2026-07-28

## Slide 8: MPEG SD Extensions
Add MPEG_anchor extension
Add MPEG_haptic and MPEG_haptic_material
Add MPEG_interactivity extension
Add MPEG_lights_* extensions
Add MPEG_primitive_V3C
Add MPEG_sampler_ycbcr
Add MPEG_material_stereo
Add MPEG_node_avatar
Add MPEG Gaussian Splats extension

## Slide 9: MPEG_anchor https://github.com/KhronosGroup/glTF/pull/2575

## Slide 10: MPEG_anchor
Enables the insertion of virtual content into the user’s real environment
Relies on the concept of trackable and anchor as defined in ETSI ARF
Provides semantics at anchor level to place the virtual assets, to launch an action when anchored, to reference a light, and to define which digital representation of the user’s environment around that anchor is recommended (e.g., which real object to detect and represent)
Trackable
real-world object that can be tracked by the XR runtime
Anchor
Virtual element having a fixed pose related
to a trackable
Several types of Trackables
controller
plane
marker
geospatial

## Slide 11: MPEG_anchor
{
…
"extensions": {
"MPEG_anchor": {
"anchors": [
{
"trackable": 0,
"requiresAnchoring":true,
"actions" :[0]
}
],
"trackables": [
{
"type": 0 // TRACKABLE_FLOOR
}
]
}
},
"scene" : 0,
"scenes" : [
{
"name" : "Scene",
"nodes" : [0,1,2,4],
"extensions": {
"MPEG_anchor": {
"anchor": 0
}
}
}
]
}
…
}
Extension at glTF file level to define the trackables and anchors
Extension at glTF scene or node level to anchor the whole scene or one or more root node(s)
Anchoring at glTF scene level
Anchoring at glTF node level

## Slide 12: MPEG_haptic and MPEG_haptic_material https://github.com/KhronosGroup/glTF/pull/2502

## Slide 13: MPEG_haptic and MPEG_haptic_material
To provide the sensation of a digital touch feedback
  Force feedback, vibration, stiffness, temperature
  Need to associate haptic media with the objects of an XR scene
Numerous use cases defined by the haptics group
  Touch the surface of a wall and feel a texture
  Press a button to get stiffness feedback
  Open a door and feel friction of the door with the floor
  …

## Slide 14: MPEG_haptic and MPEG_haptic_material
...
"extensions": {
"MPEG_media": {
"media": [
{ "alternatives": [{ "uri": "collision_enter.hmpg" }] },
{ "alternatives": [{ "uri": "collision_exit.hmpg" }] }
]
},
"MPEG_haptic": {
"hapticObjects": [
{ "accessors": [0] },
{ "accessors": [1] }
]
}
},
"scenes": [{
"name": "haptic_bubble",
"nodes": [2],
"extensions": {
"MPEG_scene_interactivities": [{
"triggers": [
{ "type": 0, "nodes": [0] }, // collision: player
{ "type": 0, "nodes": [1] } // collision: obstacle
],
"actions": [
{
"type": 7, // haptic
"hapticActionNodes": [{
"node": 0,
"material_haptic_modality": [4], // vibration
"haptic_action_medias": [{
"media_index": 0,
"perception_indices": [],
"haptic_control": 0 // play
}]
}]
}
],
"behaviors": [
{ "triggers": [0,1], "actions": [0],
"triggersCombinationControl": "#0&#1",
"triggersActivationControl": 0 },
{ "triggers": [0,1], "actions": [1],
"triggersCombinationControl": "#0&#1",
"triggersActivationControl": 1 }
]
}]
}
}]
...
Two extensions:
MPEG_haptic extension
  Refer to one or more MPEG media containing the related haptic media files
MPEG_material_haptic
  Associate the haptic properties with the mesh of an object

## Slide 15: MPEG_interactivity https://github.com/KhronosGroup/glTF/pull/2503

## Slide 16: MPEG_interactivity
Basic trigger/action mechanism to address simple, media-centric interactive use cases
  Behavior = logical combination of triggers + actions to launch
Basic physics parameters (e.g., friction, restitution, mass) enabling simple physics simulations
  Additional parameters (e.g., recommendedPhysicsFrameRate, bounceThreshold) to improve the portability of the physics simulation across game engines
Several types of triggers
  Proximity,
  Visibility,
  Collision,
  User input
Several types of actions
  Activate,
  Transform,
  Block,
  Animate,
  Media,
  Manipulate,
  SetMaterial,
  SetHaptic,
  SetAvatar
Examples of behavior with each trigger type and SetMaterial action

## Slide 17: MPEG_interactivity
...
"scenes" : [
{ "name" : "Scene",
"nodes" : [0,1,2,3,4],
"extensions": {
"MPEG_scene_interactivity": {
"triggers": [
{
"type": 0, // collision
"nodes":[0,2]
}
],
"actions": [
{
"type": 6, // set material
"material":3,
"nodes":[2]
},
{
"type": 4, // media control
"media":0,
"mediaControl": 0
}
],
"behaviors": [
{ "triggers":[0], "actions":[1],
"triggersCombinationControl":"#0",
"triggersActivationControl": 0, "actionsControl":0 }
]
}
}
}
]
...
scene
mesh
accessor
MPEG_node_avatar
MPEG_media
MPEG_scene_interactivity
behaviors
{triggers [], actions []}
node
MPEG_node_interactivity
dedicated trigger parameters
dedicated physics parameters
MPEG_scene_dynamic
MPEG_viewport_recommended
animation
material
camera
MPEG_haptic
User Inputs
trigger
action
interrupt

## Slide 18: MPEG_lights_* https://github.com/KhronosGroup/glTF/pull/2576

## Slide 19: MPEG_lights_*
MPEG_lights_punctual
  Aligned with KHR_lights_punctual for light attribute definitions.
  Enables extending light nodes with:
    The nature of the light: physical, virtual, mixed light.
    An accessor to retrieve timed updated of the light attributes.
MPEG_lights_texture_based
  Aligned with EXT_lights_image_based for lighting information definitions.
  Enables ambient lighting information with:
    The nature of the lighting information physical, virtual, mixed light.
    An accessor to retrieve timed updated of light attributes.
    Projection of the specular images (equirectangular and cubemap).
    Aligned with AR API allowing retrieval of environmental maps.

## Slide 20: MPEG_primitive_V3C https://github.com/KhronosGroup/glTF/pull/2535

## Slide 21: MPEG_primitive_V3C
Developed in alignment with Visual Volumetric Video-based Coding (V3C) standard1
  In V3C, 3D object is projected onto several 2D planes
  Projection representations are packed into 2D frames and compressed using traditional video codecs
  Main components; Geometry, Attributes and Occupancy
  Atlas Metadata stream to reconstruction 3D representation from 2D textures
Extends glTF2.0 to support Texture-based primitives to describe a 3D volumetric asset
References to textures for different V3C components
Describes a buffer format for V3C atlas data
1. ISO/IEC 23090-5:2025 Information technology, Coded representation of immersive media Part 5, Online, https://www.iso.org/standard/89030.html
Occupancy
Geometry
Attributes

## Slide 22: MPEG_primitive_V3C
"meshes": [
{
"name": "v3c_mesh",
"primitives": [
{
"attributes": {
"POSITION": 0,
"COLOR_0": 1
},
"mode": 0,
"extensions": {
"MPEG_primitive_V3C": {
"_MPEG_V3C_OVD_MAP": 2,
"_MPEG_V3C_GVD_MAPS": [3, 4],
"_MPEG_V3C_AVD": [
{
"type": 0,
"maps": [5, 6]
},
{
"type": 4,
"maps": [7, 8]
}
],
"_MPEG_V3C_CONFIG": 9,
"_MPEG_V3C_AD": {
"buffer_format": "baseline",
"accessor": 10
},
"_MPEG_V3C_CAD" : {
"MIV_view_parameters" : 11
}
}
}
. . .

## Slide 23: MPEG_sampler_ycbcr https://github.com/KhronosGroup/glTF/pull/2536

## Slide 24: MPEG_sampler_YCbCr
Support to sample a texture in YCbCr chroma format
Describes properties for shader compiler to read and sample a YCbCr textyre
Properties such as colors matrix, numerical range, chroma filter, chroma offset, and swizzle property
Compatible with Vulkan YCbCr device extension
"samplers": [
{
"extensions": {
"MPEG_sampler_YCbCr": {
"ycbcrModel": "VK_SAMPLER_YCBCR_MODEL_CONVERSION_YCBCR_709",
"ycbcrRange": "VK_SAMPLER_YCBCR_RANGE_ITU_FULL",
"chromaFilter": "VK_FILTER_NEAREST",
"xchromaOffset": "VK_CHROMA_LOCATION_MIDPOINT",
"yChromaOffset": "VK_CHROMA_LOCATION_MIDPOINT",
"components": [ "VK_COMPONENT_SWIZZLE_IDENTITY",
"VK_COMPONENT_SWIZZLE_IDENTITY",
"VK_COMPONENT_SWIZZLE_IDENTITY",
"VK_COMPONENT_SWIZZLE_IDENTITY"]
}
}
}
], . . .

## Slide 25: MPEG_material_stereo https://github.com/KhronosGroup/glTF/pull/2554

## Slide 26: MPEG_material_stereo
MPEG_material_stereo is an extension of the MPEG-I Scene Description standard (ISO/IEC 23090-14) that enables native support for stereoscopic rendering by introducing layered material definitions associated with distinct eye channels. The extension defines a structured processing model in which materials aggregate multiple texture layers, including a mandatory primary reference and optional left/right eye-specific layers, allowing consistent interpretation across rendering engines.

## Slide 27: MPEG_material_stereo
"materials": [
{
"pbrMetallicRoughness": {
"baseColorTexture": {
"index": 0
},
"metallicFactor": 0.0,
"roughnessFactor": 1.0
},
"extensions": {
"MPEG_material_stereo": {
"layers": [
{
"primaryReference": true,
"texture": 0,
"eyeChannel": 0
},
{
"primaryReference": false,
"texture": 1,
"eyeChannel": 1
}
]
}
}
}
],

## Slide 28: MPEG_gaussian_splatting_transport https://github.com/KhronosGroup/glTF/pull/2573

## Slide 29: MPEG_gaussian_splatting_transport
Built on top of KHR_gaussian_splatting
Adds support for dynamic gaussian splats (4DGS)
Provides network optimization
  Layouts for progressive download
  DC from color for fallback
  Per-channel vs per-order
Support for mesh-bound gaussian splats
  Attaches a gaussian splat to a mesh primitive
  Provides face ids, weights, etc.

## Slide 30: MPEG_node_avatar
MPEG developed a standard for representing avatars: ARF
ARF is a container + document that describe all assets and components of an Avatar and is agnostic to the scene/asset format
MPEG_node_avatar integrates an ARF avatar into a scene description

## Slide 31: Resources
MPEG Vendor Extensions are MPEG_
  https://github.com/KhronosGroup/glTF/tree/main/extensions/2.0/Vendor
GitHub Repo for collecting issues
  https://github.com/MPEGGroup/glTF
MPEG-I Scene Description Whitepapers
  First edition
  Draft of second edition
Reference Player and Software: https://www.5g-mag.com/reference-tools
More tools are collected here: https://mpeg-sd.org/extensions

## Slide 32: Thank you
http://mpeg.org